SECTION 05512

CAGED ALUMINUM ACCESS LADDERS

*****  UPNOVR, Inc. manufactures several types of aluminum access ladders.  This guide specification section can be used to specify fixed, wall mounted, vertical access ladders with integral safety cages.  Ladders over 24 feet high are required to have fall protection.

******************************************************************************

PART 1 - GENERAL

1.1	SUMMARY

*****  UPNOVR, Inc. manufactures five models of caged aluminum access ladders.  Select required type in the following paragraph and delete nonapplicable types.  *****

A.	Section includes:  Fixed, wall mounted, vertical, aluminum, [roof hatch rail extension ladder with integral safety cage.] [roof over rail extension ladder with integral safety cage.] [return to rear of parapet ladder with integral safety cage.] [ladder with platform, return to rear of parapet, and integral safety cage.] [ladder with intermediate platforms, roof over rail, and integral safety cage.]

B.	Related sections:

1.	Section 06100 - Rough Carpentry:  Blocking in metal stud walls and partitions for anchorage of access ladders.

2.	Section 07725 - Roof Hatch:  Manufactured roof hatch to be accessed by aluminum ladder.

*****  Safety post extensions are often used in conjunction with roof hatch access ladders.  They can be provided separately or with ladder.  *****

3.	Section 07726 - Ladder Safety Post Extension:  UPNOVR safety post extension to be attached to roof access ladder.

1.2	REFERENCES

A.	American National Standards Institute (ANSI):

1.	ANSI A14.3 - Ladders, Fixed, Safety Requirements.

B.	American Society for Testing and Materials (ASTM) Publications:

1.	ASTM B209 - Aluminum and Aluminum-Alloy Sheet and Plate.

2.	ASTM B221 - Aluminum-Alloy Extruded Bar, Rod, Wire, Shape, and Tube.

C.   Occupational Safety and Health Administration of the Unites States

- OHSA 1910.23: Fixed Ladders

- OSHA 1910.28: Duty to have fall protection and falling object protection

1.3	SUBMITTALS

A.	Provide in accordance with Section 01330 - Submittal Procedures:

1.	Product data for access ladders and accessories.

2.	Shop drawings showing elevations, dimensions, and fabrication details.

3.	Installation and maintenance instructions.

1.4	QUALITY ASSURANCE

A.	Manufacturer Qualifications:  Ladders to be provided by single manufacturer with minimum of five years of experience in metal ladder fabrication.

B.  Access ladders shall be designed and installed to comply with ANSI A14.3. and OSHA 1910.27 minimum standards.

PART 2 - PRODUCTS

2.1	ACCEPTABLE MANUFACTURERS

A.	UPNOVR, Inc., PO Box 199, Pelham, New Hampshire 03076; 603-625-8639.

B.	Substitutions not permitted

2.2	MATERIALS

A.	Extruded aluminum:  ASTM B221, Alloy 6061 Temper T-6, non-spark.

B.	Sheet aluminum:  ASTM B209 6061 Temper T-6.

*****  Standard access ladder finish is mill finished aluminum.*****

C.	Finish:  Mill finished aluminum.

2.3	GENERAL FABRICATION

A.	Field verify ladder dimensions prior to fabrication.

B.	Fabricate to designs indicated on Drawings and to meet performance requirements specified in Paragraph 1.4.

C.	Ladder rungs shall be welded.  Ladders longer than 15ft will be shipped in sections.

2.4	VERTICAL CAGED ACCESS LADDER

*****  UPNOVR, Inc. manufacturers 5 models of fixed, wall mounted, vertical access ladders with integral safety cages.  Select required type from the following options and delete non-applicable options.  *****

A.	Type:  Fixed, wall mounted, vertical, caged, aluminum, [roof hatch rail extension ladder; Model No. U-300] [roof over rail extension ladder; Model No. U- 301] [return to rear of parapet ladder; Model No. U-302] [ladder with platform and return to rear of parapet; Model No. U-303] [ladder with intermediate platforms and roof over rail; Model No. U-390] as manufactured by UPNOVR, Inc.

*****  Include the following paragraphs to specify caged roof hatch ladder;

Model No. U-300.  Ladders over 24 feet high are required to have fall protection.  *****

B.	Nominal height:  [[_____] feet.] [As indicated on Drawings.]

C.	Side rails:  1-3/4 inches by 3 inches tubes with 1/8 inch wall thickness.

*****  Rung width for caged access ladders is 24 inches. *****

D.	Rungs:  1-1/4 wide by 1-1/4 inches tube by 24 inches long with corrugated surfaces and capable of 1,000 pounds load.  Space 12 inches on center.  Attach rungs in centerline of side rails by welding.

*****  Include the following paragraphs to specify caged roof over rail extension ladder; Model No. U-301.  Ladders over 24 feet high are required to have fall protection.  *****

B.	Nominal height:  [[_____] feet.] [As indicated on Drawings.]

C.	Side rails:  1-3/4 inches by 3 inches tubes with 1/8 inch wall thickness.  Extend rails 42 inches above [roof line.] [parapet.]

D.	Extension:  At top of side rails provide 19 inches extension, 28 inches high, constructed from 1-1/4 inches square tube grab bars with corrugated surfaces.

*****  Rung width for caged access ladders is 24 inches. *****

E.	Rungs:  1-1/4 inches square tube by 24 inches long with corrugated surfaces and capable of 1,000 pounds load.  Space 12 inches on center.  Attach rungs in centerline of side rails by welding.

*****  Include the following paragraphs to specify caged return to rear of parapet ladder; Model No. U-302.  Ladders over 24 feet high are required to have fall protection.  *****

B.	Nominal height:  [[_____] feet.] [As indicated on Drawings.]

*****  Cross

over span will be determined by width of parapet wall.  *****

C.	Cross over span:  [[_____] inches.] [As indicated on Drawings.]

D.	Side rails:  1-3/4 inches by 3 inches tubes with 1/8 inch wall thickness.  Extend rails 42 inches above parapet.  Provide rails on opposite side mounted to rear of parapet and extending 42 inches above parapet and below parapet to roof line.

E.	Grab bars:  Connect front and rear side rails 1-1/4 inch square tube grab bars with corrugated surfaces.

*****  Rung width for caged access ladders is 24 inches. *****

F.	Rungs:  1-1/4 inches square tube by 24 inches long with corrugated surfaces and capable of 1,000 pounds load.  Space 12 inches on center.  Attach rungs in centerline of side rails by welding.

*****  Include the following paragraphs to specify caged ladder with platform and return to rear of parapet; Model No. U-303.  Ladders over 24 feet high are required to have fall protection.  *****

B.	Nominal height:  [[_____] feet.] [As indicated on Drawings.]

*****  Cross over span will be determined by width of parapet wall.  *****

C.	Cross over span:  [[_____] inches.] [As indicated on Drawings.]

D.	Side rails:  1-3/4 inches by 3 inches tubes with 1/8 inch wall thickness.  Extend rails 42 inches above parapet.  Provide rails on opposite side mounted to rear of parapet and extending 42 inches above parapet and below parapet to roof line.

E.	Grab bars:  Connect front and rear side rails with 1-1/4 inch square tube grab bars with corrugated surfaces.

F.	Platform:  Provide cross over platform fabricated from 6 inches wide by 1-3/4 inches deep aluminum treads with corrugated surface.

*****  Rung width for caged access ladders is 24 inches. *****

G.	Rungs:  1-1/4 inches square tube by 24 inches long with corrugated surfaces and capable of 1,000 pounds load.  Space 12 inches on center.  Attach rungs in centerline of side rails by welding.

*****  Include the following paragraphs to specify caged roof over rail extension ladder with intermediate platforms; Model No. U-390.  Ladders over 24 feet high are required to have fall protection.  *****

B.	Configuration:  Ladder shall be configured with [2] [_____] caged vertical ladder segments offset from each other and connected with intermediate platform with guardrail as indicated on Drawings.  Nominal heights of ladder segments:

1.	Lower segment:  [_____] feet.

2.	Upper segment:  [_____] feet.

C.	Side rails:  1-3/4 inches by 3 inches tubes with 1/8 inch wall thickness.  Extend rails of upper ladder segment 42 inches above [roof line.] [parapet.]

D.	Extension:  At top of upper segment side rails provide 19 inches extension, 28 inches high.  Construct from 1-1/4 inches square tube grab bars with corrugated surfaces.

*****  Rung width for caged access ladders is 24 inches. *****

E.	Rungs:  1-1/4 inches square tube by 24 inches long with corrugated surfaces and capable of 1,000 pounds load.  Space 12 inches on center.  Attach rungs in centerline of side rails by welding.

F.	Intermediate platform:  Provide intermediate cross over platform fabricated from 6 inches wide by 1-3/4 inches deep aluminum treads with corrugated surface.

G.	Guardrail:  At intermediate platform provide guardrail constructed from 1-1/4 inches square tube grab bars with corrugated surfaces.  Guardrail shall be 42 inches high and connect side rails of two ladder segments as detailed on Drawings and reviewed shop drawings.

2.5	SAFETY CAGE

A.	Equip ladders with safety cages as detailed on Drawings and reviewed shop drawings.

B.	Fabricate from 2 inches wide by 1/4 inch thick aluminum vertical strips and horizontal loops welded to form cage around ladder.

1.	Bottom loop radius:  17-1/2 inches.

2.	Radius of other loops:  13-1/2 inches.

3.	Provide 7 vertical strips equally spaced around perimeter of cage.

4.	Space horizontal loops at 48 inches maximum.

C.	Minimum clearance from ladder to back of cage:  27 inches.

D.	Start cage [7] [8] [_____] feet above [grade] [intermediate platform] [roof level].

E.	Extend safety cage 42 inches minimum above top rung and attach to side rails as detailed on Drawings and reviewed shop drawings.

F.   Safety cage to ship knocked down with connection hardware for field assembly

G.  At customer request ladder cage can be shipped as a fully welded assembly mounted to ladder.

2.6	ACCESSORIES

A.	Support brackets:

1.	Wall brackets:  Support ladder at top and bottom and at 48 inches maximum intermediate points with 2 by 1/4 inch minimum flat bar aluminum wall brackets.  Allow 7 inches minimum clearance from wall to center line of rungs.

*****  As an option, a hinged security door can be provided to cover bottom ladder rungs and prevent unauthorized roof access.  Include the following paragraph for this option.  *****

B.	Security door:  Provide hinged security door to cover bottom rungs and prevent unauthorized roof access.

1.	Construction:  Fabricate from 11 gage flat aluminum sheet covering front of ladder.  Provide side flanges extending toward wall and meeting aluminum flange mounted to wall.

2.	Equip door with continuous stainless steel hinge and padlock hasp.

*****  Safety post extension can be provided in conjunction with roof hatch and specified in other sections.  As an option, safety post extension can be provided by UPNOVR, Inc. with access ladder.  Include the following paragraph to specify this option.  *****

C.	Safety post extension:  Post extension for fixed ladders constructed of tubular aluminum sections with adjustable mounting brackets for attachment to top of ladder.

1.	Operation:  Upward and downward movement controlled by operator.  Post locks when fully extended.

2.	Use in accordance with manufacturer’s instructions.

PART 3 - EXECUTION

3.1	PREPARATION

A.	Prior to fabrication, field verify required dimensions.

B.	Coordinate provision of access ladder with provision of roof hatch specified in Section 07725 - Roof Hatch to ensure height and position of ladder is compatible with roof hatch curb.

C.	Coordinate ladder installation with construction of [CMU walls specified in Section 04220 - Concrete Unit Masonry to ensure block walls are adequately reinforced and cells grouted] [metal stud walls specified in Section 05400 - Cold Formed Metal Framing to ensure adequate support and blocking] [stud partitions specified in Section 09260 - Gypsum Board Assemblies to ensure adequate support and blocking] for attachment of brackets and support of ladder.

D.	Insulate dissimilar metals to prevent electrolysis with bituminous paint or non-absorptive isolation pad to prevent contact.

3.2	INSTALLATION

A.	Install ladder and safety cage in accordance with manufacturer's instructions and reviewed shop drawings.

B.	Position ladder such that side rails end 3 inches above floor and center of rungs are a minimum of 7 inches from wall.

C.	Securely anchor support brackets with fasteners of type specified under other sections.  Place wall brackets at top and bottom of ladder.  Place intermediate wall brackets at 48 inches maximum.

D.	Ensure ladder and safety cage are vertical, plumb, [aligned with center of roof hatch,] and rigid.

*****  Include the following paragraph is security door is required.  *****

E.	Install security door assembly and adjust for smooth operation.

*****  Include the following paragraph if safety post extension is required.  *****

1.	Safety post extension:  Attach to top 2 rungs of ladder and centered between side rails.  Adjust post to extend 42 inches above top rung when roof hatch is open and post is fully extended.

2.	After installation inspect ladder to verify proper, secure, and safe installation.

3.	Clean ladder using clean water and mild detergent.  Do not use abrasive agent, steel wool, or harsh chemicals.  Rinse with clean water.

END OF SECTION